Operational Information

1967 Cherokee C

N4833L

Limitations

Utility category:

- 2000 pounds

- 4.4g, -1.76g

- Chandelles/lazy eights/steep turns: 110 KIAS

Normal Category

- 2400 pounds

- 3.8g, -1.76 g

V Speeds

|  |  | MPH |
| --- | --- | --- |
| Vglide |  | 80 |
| Vx |  | 74 |
| Vy |  | 85 |
| Vcc |  | 100 |
| Vso |  | 57 |
| Vs |  | 66 |
| Vne |  | 171 |
| Vno |  | 140 |
| Va |  | 129 |
| Vfe |  | 115 |
| Pattern |  | 90/80/70 |

Traffic Pattern:

Abeam

- 1500 RPM

- 10° flaps

- 90 MPH (1 notch)

Base

- 25° flaps (2 notches)

- 80 MPH

Final

- 40° flaps (3 notches)

- 70 MPH

Short landing

- 40°flaps

- 65 MPH

Systems

Fuel System

- 2 tanks/25 gallons each/ 50 gallons total

- 24 gallons usable/1.0 gallon unusable per tank

- 2 fuel vents/3 fuel drains

- Tabs-17 gallons each side

- ¼ indication: 5 gallons left in tank

- Switch tanks every 30 minutes

Electrical System

- 14 volt system

- Alternator

- No Alternator switch/Master only

Engine

- Lycoming 0-360-A2A

- 180 HP@ 2700 RPM

- Static RPM: 2300 RPM

- 8 Quarts Oil/5 minimum  KEEP AT 6 QUARTS

- Preheat below 20°F

- Engine oil pressure 30-60 PSI/10 PSI minimum at idle

- 75% power

Sea level	2450 RPM			5000 ft.	2550 RPM

2500 ft.	2500 RPM			7500 ft.	2600 RPM

- Carburetor heat-ON as required below 2000 RPM

Weight & Balance

- 2400# Gross weight Normal category

- 2000# Gross weight Utility category

- 1019# useful load

- 125# baggage compartment

Tire pressure

- 24 PSI Nose

- 24 PSI Main

Leaning in flight

- Set power/RPM

- Pull mixture control aft until a slight drop in RPM is detected/EGT peaks-this is the lean position

- Enrichen mixture until the EGT drops a minimum of 25° from the lean position and RPM returns and is smooth.

Differences

- Brakes-there are toe brakes on the pilot side only, and a single brake lever.

  - Door latch-there is only an upper door latch

  - The cabin vent window can be opened in flight

  - Please use seat cushions to assist in adjusting seating height